## Slide 1: Presales training

## Slide 2: Workshop session

## Slide 3: Useful resources
Questions ? http://ask.sigfox.com
Github http://github.com/sigfox/makers-tour-resources
Github http://github.com/nicolsc
Smarteverything : http://www.smarteverything.it/
Telit LE51-868s guides : http://www.telit.com/sr-rf/le51-868-s/
User guides -> Software user guide

## Slide 4: Payload examples
GPS coordinates (lat x lng) : 6 bytes
Temperature: 2 bytes
State reporting : 1 byte
Heartbeat, update request : 0 byte
And … who needs full bytes when 5 bits are enough ?

## Slide 5: Real life example
http://www.adeunis-rf.com/media/downloads/181/trad_file/fre/arf8047xx_sigfox_sensors_user_guide_v2.0.1-fr-gb.pdf

## Slide 6: Arduino 101
2 main functions : setup(), infinite loop()
Librairies to be #include first:
arduino.h
wire.h
SerialUSB.begin -> initiate serial
SerialUSB.print / prinln -> print to serial monitor

## Slide 7: ACTIVATE DEVICE
Enter type : Smarteverything
Country : France
Device ID : (sticker on the back)
PAC –> Unique activation code (ask me)
Create an account.
(For non dev kits :
Create a new device type
Create a new device with ID and PAC and put it in the device type. )
For dev kits : https://backend.sigfox.com/activate

## Slide 8: HELLO WORLD CAFE

## Slide 9: SmartEverything test
Open the Arduino IDE
Select the Board type : Smart Everything Fox (USB)
Select the com port
Create a new (empty) file, compile and upload to the board. Works ?
Now add Serial + Sigfox initialization, put the Telit module in command mode and use SigFox.print to send AT command to Telit module (lookup software guide for AT command references). Don’t forget to SigFox.print(« \r") after.

## Slide 10: Message received ?
https://backend.sigfox.com
Navigate to the devices menu in the top bar
Click on the ID of your device
Enter the messages menu from the left navigation column

## Slide 11: First callback

## Slide 12: Callback setup #1
Device Type menu
Click on your device type name
Enter the Callbacks menu
Select new default callback

## Slide 13: Callback setup #2
TYPE : DATA UPLINK
Choose a CHANNEL : URL (EMAIL for a quick test)
Url pattern: URL of your own server
Use HTTP method: GET/POST/PUT

## Slide 14: Callback status
In the Devices > Messages panel, you have a indicator of the callback status (an arrow)
  Black : in progress
  Green : Callback OK
  Red : Callback KO (at least one of the callbacks failed)
Click the arrow to display details.

## Slide 15: Run it !
Reset your board for another run, you should see the callback coming out. Check on the backend for status.

## Slide 16: Downlink

## Slide 17: How does it work ?
Send a message, with a downlink flag
Once message is sent, the module gets back to sleep
After 20s, it will wake up automatically, in Rx mode
It will wait 20s for a downlink message
Afterwards it will get back to sleep

## Slide 18: Downlink test setup
To setup an automatic callback :
  Device Type > click on the device type chosen > Edit
  In the Downlink data settings, set the following :
    Downlink Mode : DIRECT
    Set the value

## Slide 19: How to request a downlink
Same AT command, with additional parameters
AT$SF=[hex byte]*, 1
In the main loop, read the input from SigFox and display to Serial.
RSSI value : http://www.binaryhexconverter.com/decimal-to-hex-converter

## Slide 20: Real data

## Slide 21: Read data from Temperature sensor
Look at example file !
#include HTS221.h
Wire.begin();
smeHumidity.begin();
Then temperature = smeHumidity.readTemperature();